## Slide 1: Impact of Multi-View Fusion and Biomechanical Modeling on Markerless Motion Tracking
Review – 20/11/2025

## Slide 2
1 - Impact of biomechanical modelisation | 2 - Multi-view vs Single-view
Biomechanical model  = Hard joint constraints | 
Key Hypotheses
13 single-view methods
2 multi-view methods
Theida 3D
OpenCap
( ≈ MOCAPIA)
SMPL model (Skinned Multi-Person Linear model)
= Soft joint constraints
SMPL model + OpenSim
SMPL model
VS
What gains justify switching technology?
Only on single-view methods !!

## Slide 3
DATA process
Marker Solution (reference)
20 IR cameras 100Hz 45 physical markers A wand calibration
Markerless Solution
20 RGB cameras 100Hz Calibration board
23 participants – controlled indoor environments
Single-View methods
- All of them are based the SMPL model
Multi-View methods | 
OpenCap | Theida 3D
No SMPL model But a IK correction with OpenSim | 
Use a static pose to prevent a discrepancy between physical and virtual markers

## Slide 4: Tools of evaluation
RMSD (Root Mean Square Difference)
A biomechanical tool
PA-MPJPE
A computer-vision tool
Linear Mixed-Effects Model + ANOVA III
LMEM: split the fix effects(motion capture methods) and random effects (size, weight of the subject)
ANOVA: evaluate if the result (RMSD) is statistically true (

## Slide 5: Process 2/4 – Primary evaluation
Evaluation of 13 single view methods
Evaluated across all 10 cameras – 33Hz (same as us) Average RMSD across all views after a Kruskal-Wallis test WHAM achieved the lowest RMSD with 7.6°

## Slide 6: Results- hypothese 1
WHAM model
(camera 7)
WHAM model
(camera 7)
Use of the SMPL model on WHAM
Use of the SMPL model on WHAM
29 markers used for
OpenSim IK
bioWHAM
WHAM with «soft» constraints

## Slide 7: Process 4/4 – Hypothese 2
OpenCap
90°
The same calibration is used for OpenCap et Theia3D – no reprojection error study
Calibration
2 cameras
No accuracy gains by adding cameras
Estimateur de pose 2D | 
HRNet | OpenPose
Considered less accurate than RTMPose (used in MoCapIA) | 
filtering
triangulation
Marker Augmentation
IK on OpenSim

## Slide 8: Results– Hypothese 2
Theia3D
10 cameras – 6 cameras min
Black-Box
(private licence)
OpenCap
WHAM/bioWHAM

## Slide 9: Auxiliary Finding
Correlation between RMSD and PA-MPJPE
An metric used in the field of computer vision
An metric used in the field of biomechanic
Datasets | 
3DPW | I-MOVE-23
Standart reference dataset in CV | data collected for this study
Conclusion
Both metrics are highly correlated
Both of them could be used in MoCapIA’s project